## Slide 1: Micro-network-project
Xiaoguang Guo

## Slide 2: Outline
1. Overview
2. System Design and Pipeline
3. Existing Works
4. Inference Performance Predictor
5. Insights
6. Search

## Slide 3: 1. Overview
The goal is to optimize the partitioning of DNN models across resource-limited MCU nodes in a BLE mesh network without internet connectivity, focusing on minimizing computation and transfer time while considering memory and energy constraints.
This involves:
  1. How to make multiple MCUs cooperate?
    WiFi and BLE-Mesh
  2. How to run inference on multiple MCUs?
    Model Partitioning

## Slide 4: 2.1 System Design
1. Network Construction
  Network topology
  Roles assignment
  Link
Scheduler
Communication API
Scheduler:
  1. Preconfigure the network
  2. Model partitioning and deployment
  3. Monitor the network (feedback loop)

## Slide 5: 2.1 System Design
Distributed Inference/retraining
Collaborative Virtual Network Our new virtual network
BLE 1.1 Mesh Network
We will use computing/super nodes to establish the distributed learning path on the overlay network.

## Slide 6: 2. 2 Pipeline
1. Network Initialization
2. Profiling
  Network conditions:
    Nodes capabilities(CPU, Memory, Architecture)->processing time
    Network bandwidth -> transfer time
  DNN Model (per layer)
    Latency, memory, energy, data size
3. Model Partitioning
  Per layer execution time (Assume that each layer is independent)
  Assignment(layer-device) determination
4. Model Deployment
  Select virtual ‘routing’ for distributed inference
5. Optimization (optional)
  Feedback loop (Network <-> Model performance)
  Model optimization

## Slide 7
BLE Mesh Network
Overlay Network
Model Partitioning
Scheduler
Profiler
Search
Inference performance predictor for MCUs
Latency
Memory
Energy
Network Conditions
Profiler
Bandwidth
Nodes Capabilities
Routing
Provisioning
Flooding
Data Size
Relaying

## Slide 8: 2. 3 Model Partitioning Pipeline
Determination of assignment(layer-device): (search problem)
  Input(network, model)
    Network(nodes,)
    Model(layers,)
  Output(assignment)
Model partition:
  Input(assignment, model)
  Output(model segment 1, model segment 2)
Model deployment:
  Model segment 1 -> MCU 1
  Model segment 2 -> MCU 2
  ……

## Slide 9: 3. Distributed Inference
Notes: [1]: Alonso, Tobias, Lucian Petrica, Mario Ruiz, Jakoba Petri-Koenig, Yaman Umuroglu, Ioannis Stamelos, Elias Koromilas, Michaela Blott, and Kees Vissers. "Elastic-df: Scaling performance of dnn inference in fpga clouds through automatic partitioning." ACM Transactions on Reconfigurable Technology and Systems (TRETS) 15, no. 2 (2021): 1-34.

## Slide 10: 3.1 Model Partitioning Existing Works(Edge - Cloud)
Neurosurgeon(ASPLOS’17)[1]:
  Analyze DNN Architecture-> Predict Layer Performance->Evaluate Partition Points->Execute Partitioned DNN
DADS(INFOCOM’19)[2]: Min-Cut
QDMP(IMWUT’20)[3]: Per layer latency is calculated by subtracting the maximum latency of all precursor layers from the total latency up to the current layer.
Auto-Split(KDD’21 ADS Track)[4]: Graph Optimization(Layer folding, layer fusion)
Notes: [1] Kang, Y., Hauswald, J., Gao, C., Rovinski, A., Mudge, T., Mars, J., & Tang, L. (2017). Neurosurgeon: Collaborative intelligence between the cloud and mobile edge. ACM SIGARCH Computer Architecture News, 45(1), 615-629.
[2] Hu, Chuang, Wei Bao, Dan Wang, and Fengming Liu. "Dynamic adaptive DNN surgery for inference acceleration on the edge." In IEEE INFOCOM 2019-IEEE Conference on Computer Communications, pp. 1423-1431. IEEE, 2019.
[3] Zhang, Shigeng, Yinggang Li, Xuan Liu, Song Guo, Weiping Wang, Jianxin Wang, Bo Ding, and Di Wu. "Towards real-time cooperative deep inference over the cloud and edge end devices." Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies 4, no. 2 (2020): 1-24.
[4] Banitalebi-Dehkordi, Amin, Naveen Vedula, Jian Pei, Fei Xia, Lanjun Wang, and Yong Zhang. "Auto-split: A general framework of collaborative edge-cloud AI." In Proceedings of the 27th ACM SIGKDD Conference on Knowledge Discovery & Data Mining, pp. 2543-2553. 2021.

## Slide 11: 3.2 Model Partitioning Existing Works(Three-tier)
DECC[1]: Iteration
PSO-GA:
  Cloud-Edge-End[2]
  VEC[3]: Vehicles - Edge servers – Service vehicles
DNNSplit[4]:
  Greedy Search
  Deployment cost
Notes: [1]: Chen, Jianan, Qi Qi, Jingyu Wang, Haifeng Sun, and Jianxin Liao. "Accelerating dnn inference by edge-cloud collaboration." In 2021 IEEE International Performance, Computing, and Communications Conference (IPCCC), pp. 1-7. IEEE, 2021.
[2]: Lin, Bing, Yinhao Huang, Jianshan Zhang, Junqin Hu, Xing Chen, and Jun Li. "Cost-driven off-loading for DNN-based applications over cloud, edge, and end devices." IEEE Transactions on Industrial Informatics 16, no. 8 (2019): 5456-5466.
[3]: Li, Chunlin, Long Chai, Kun Jiang, Yong Zhang, Jun Liu, and Shaohua Wan. "DNN partition and offloading strategy with improved particle swarm genetic algorithm in VEC." IEEE Transactions on Intelligent Vehicles (2023).
[4]: Kayal, Paridhika, and Alberto Leon-Garcia. "DNNSplit: Latency and Cost-efficient Split Point Identification for Multi-tier DNN Partitioning." IEEE Access (2024).

## Slide 12: 3.3 Inference Performance Predictor Existing Works
LPM-TPU[1]
NP-NAS[2]
BRP-NAS (Eagle)[3]
nn-Meter[4]
PerfSAGE[5]
Notes: [1]: Kaufman, S., Phothilimthana, P., Zhou, Y., Mendis, C., Roy, S., Sabne, A., and Burrows, M. A learned performance model for tensor processing units. Proceedings of Machine Learning and Systems, 3:387–400, 2021.
[2]: Wen, Wei, Hanxiao Liu, Yiran Chen, Hai Li, Gabriel Bender, and Pieter-Jan Kindermans. "Neural predictor for neural architecture search." In European Conference on Computer Vision, pp. 660-676. Cham: Springer International Publishing, 2020.
[3]: Dudziak, Lukasz, Thomas Chau, Mohamed Abdelfattah, Royson Lee, Hyeji Kim, and Nicholas Lane. "Brp-nas: Prediction-based nas using gcns." Advances in Neural Information Processing Systems 33 (2020): 10480-10490.
[4]: Zhang, Li Lyna, Shihao Han, Jianyu Wei, Ningxin Zheng, Ting Cao, Yuqing Yang, and Yunxin Liu. "Nn-meter: Towards accurate latency prediction of deep-learning model inference on diverse edge devices." In Proceedings of the 19th Annual International Conference on Mobile Systems, Applications, and Services, pp. 81-93. 2021.
[5]: Chai, Yuji, Devashree Tripathy, Chuteng Zhou, Dibakar Gope, Igor Fedorov, Ramon Matas, David Brooks, Gu-Yeon Wei, and Paul Whatmough. "Perfsage: Generalized inference performance predictor for arbitrary deep learning models on edge devices." arXiv preprint arXiv:2301.10999 (2023).

## Slide 13: 3.4 Inference Performance Predictor Existing Works
MicroNets[1]:
TinyMLPerf[2]: overall performance of TinyML models.
Regression model
Notes: [1]: Banbury, C., Zhou, C., Fedorov, I., Matas, R., Thakker, U., Gope, D., ... & Whatmough, P. (2021). Micronets: Neural network architectures for deploying tinyml applications on commodity microcontrollers. Proceedings of machine learning and systems, 3, 517-532.
[2]: Banbury, Colby R., Vijay Janapa Reddi, Max Lam, William Fu, Amin Fazel, Jeremy Holleman, Xinyuan Huang et al. "Benchmarking tinyml systems: Challenges and direction." arXiv preprint arXiv:2003.04821 (2020).

## Slide 14: 4. Inference Performance Predictor
Datasets
  Latency datasets:
    The latency for various MCUs, across different types of layers and sizes, is measured using TensorFlow Lite for Microcontrollers (TFLM).
  Memory footprint datasets:
    Simulation on Server?
  Energy consumption datasets:
Predictor(MCU, Layer) =
  Latency
  Memory footprint (memory, storage)
  Energy consumption
Notes: [1]: Banbury, C., Zhou, C., Fedorov, I., Matas, R., Thakker, U., Gope, D., ... & Whatmough, P. (2021). Micronets: Neural network architectures for deploying tinyml applications on commodity microcontrollers. Proceedings of machine learning and systems, 3, 517-532.

## Slide 15: 5. Insights
1. Per layer latency
2. Data size distribution
Notes: [1]: Zhang, Shigeng, Yinggang Li, Xuan Liu, Song Guo, Weiping Wang, Jianxin Wang, Bo Ding, and Di Wu. "Towards real-time cooperative deep inference over the cloud and edge end devices." Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies 4, no. 2 (2020): 1-24.
[2]: Liang, Huanghuang, Qianlong Sang, Chuang Hu, Dazhao Cheng, Xiaobo Zhou, Dan Wang, Wei Bao, and Yu Wang. "DNN surgery: Accelerating DNN inference on the edge through layer partitioning." IEEE transactions on Cloud Computing 11, no. 3 (2023): 3111-3125.

## Slide 16: 5. Insights
1. Per layer latency
  As much as possible, concentrate multiple layers on one single node
    Reduce transferring time
    Utilize cross-optimization
2. Data size distribution
  High memory: model parallel distribution (Layer-Partitioning )
  High computation and low memory: data parallel distribution (maybe in optimization step)
3. Layer types:
  After Pooling Layers: Pooling layers reduce the dimensionality of the data
  After Dense Layers: Small output

## Slide 17: 6. Search
Cost Function: multi-objectives search
.
Linear:
Or non-linear:

## Slide 18: MILP
Binary Assignment Variables
Energy Variables
Time Variables
Objective function

## Slide 19: 6. Search
Computation and transfer time:
1. Layer-Device Assignment Matrix (X)
  Represents which device each layer is assigned to.
  Rows correspond to layers, and columns correspond to devices.
  A ‘1’ in the matrix indicates the layer is assigned to that device.
2. Transfer Time Matrix (T)
  Represents the time required to transfer data between devices.
  Rows and columns correspond to devices.
  An element T[i,j] indicates the time to transfer data from Device i to device j.
3. Computation Time Matrix (C)
  An element C[i,j] indicates the computation time that device j process layer i

## Slide 20: 6. Search Methods
Greedy Algorithm
Simulated Annealing
Genetic Algorithm
Particle Swarm Optimization
Ant Colony Optimization
Branch and Bound
Hill Climbing
Random Search
Mixed-Integer Linear Programming
Tabu Search
Table: Performance Comparison of Different Partitioning Algorithms for Layer-Device Assignment in Distributed Inference on a 6-Layer Model Across 5 Devices

## Slide 21
Multiple partitioning solutions
  Pre-compute Multiple Solutions
  Store locally
    To handle with node failures or dynamic changes
Redundancy through
  Store extra layers
  Predefined backup paths
  Dynamic Reassignment

## Slide 22: Local scheduler
Monitor Task Execution:
  Ensure that inference tasks are proceeding as expected.
Monitor Task Queue:
  ensure that tasks are processed in order of priority.
Sync?
Handle Timeouts/Failures:
  Detect if tasks fail to execute within expected timeframes

## Slide 23: Local Scheduler Pipeline
1. Task Scheduling & Execution

## Slide 24: Questions
1. Per layer execution time
2. Feedback: model <-> network
2. How to evaluate search methods?
4. Contributions
5. Deployment cost
6. tflite optimization

## Slide 25: Latency Estimation
Hardware:
  Processor
  Persistent program memory (Flash)
  Volatile static RAM
On a different device, the same operator can have different latency.

## Slide 26: Energy Estimation

## Slide 27: Workflow
1. Build and train a model using `TensorFlow`
2. Convert the TensorFlow model to a `.tflite` file using `TFLiteConverter`
3. Apply optimizations like `quantization`, `pruning`, `operator`. (Optional)
Profiling MACs
4. Adapt the TensorFlow Lite Model for TensorFlow Lite Micro.
  Model structure is not modified

## Slide 28: Model Generator
Model Converter:
  Load Pre-trained Model
  Optional Modifications
  Convert the Model