## Slide 1: Micro-network-project
Xiaoguang Guo

## Slide 2: Overview
The goal is to optimize the partitioning of DNN models across resource-limited MCU nodes in a BLE mesh network without internet connectivity, focusing on minimizing computation and transfer time while considering memory and energy constraints.
This involves:
1. Building an overlay network(BLE)
2. Implementing distributed inference strategies. (layer-based)

## Slide 3: Motivations
Internet-less decentralized network
  Applications: underground mining, deep sea, mountains, UAVs
Distributed inference on embedding system
  Leverage resources from multiple devices (data, processor)

## Slide 4: Overlay network (p2p as an example)
Distributed Inference/retraining
Collaborative Virtual Network Our new virtual network
BLE 1.1 Mesh Network
We will use computing/super nodes to establish the distributed learning path on the overlay network.

## Slide 5
BLE Mesh Network
Overlay Network
Model Partitioning
Scheduler
Profiler
Search
Inference performance predictor for MCUs
Latency
Memory
Energy
Network Conditions
Profiler
Bandwidth
Nodes Capabilities
Routing
Provisioning
Forwarding

## Slide 6: Pipeline
1. Network Profiling
  Nodes capabilities(CPU, Memory, Architecture)->processing time
  Network bandwidth -> transfer time
2. Model Partitioning
  Per layer execution time (Assume that each layer is independent)
  Assignment(layer-device) determination
3. Model Deployment
  Select virtual ‘routing’ for distributed inference
  (Does the model also affect the construction of the network?)

## Slide 7: Model Partitioning Pipeline
Determination of assignment(layer-device): (search problem)
  Input(network, model)
    Network(nodes,)
    Model(layers,)
  Output(assignment)
Model partition:
  Input(assignment, model)
  Output(model segment 1, model segment 2)
Model deployment:
  Model segment 1 -> MCU 1
  Model segment 2 -> MCU 2
  ……

## Slide 8: Computation and transfer time
1. Layer-Device Assignment Matrix (X)
  Represents which device each layer is assigned to.
  Rows correspond to layers, and columns correspond to devices.
  A ‘1’ in the matrix indicates the layer is assigned to that device.
2. Transfer Time Matrix (T)
  Represents the time required to transfer data between devices.
  Rows and columns correspond to devices.
  An element T[i,j] indicates the time to transfer data from Device i to device j.
3. Computation Time Matrix (C)
  An element C[i,j] indicates the computation time that device j process layer i

## Slide 9: Search Methods
Greedy Algorithm
Simulated Annealing
Genetic Algorithm
Particle Swarm Optimization
Ant Colony Optimization
Branch and Bound
Hill Climbing
Random Search
Mixed-Integer Linear Programming
Tabu Search
Table: Performance Comparison of Different Partitioning Algorithms for Layer-Device Assignment in Distributed Inference on a 6-Layer Model Across 5 Devices

## Slide 10: Model Partitioning Existing Works
Applicable Scenarios: Edge-Cloud
Neurosurgeon(ASPLOS’17)[1]:
  Analyze DNN Architecture-> Predict Layer Performance->Evaluate Partition Points->Execute Partitioned DNN
DADS(INFOCOM’19)[2]: Min-Cut
QDMP(IMWUT’20)[3]: Per layer latency is calculated by subtracting the maximum latency of all precursor layers from the total latency up to the current layer.
Auto-Split(KDD’21 ADS Track)[4]: Graph Optimization(Layer folding, layer fusion)
Notes: [1] Kang, Y., Hauswald, J., Gao, C., Rovinski, A., Mudge, T., Mars, J., & Tang, L. (2017). Neurosurgeon: Collaborative intelligence between the cloud and mobile edge. ACM SIGARCH Computer Architecture News, 45(1), 615-629.
[2] Hu, Chuang, Wei Bao, Dan Wang, and Fengming Liu. "Dynamic adaptive DNN surgery for inference acceleration on the edge." In IEEE INFOCOM 2019-IEEE Conference on Computer Communications, pp. 1423-1431. IEEE, 2019.
[3] Zhang, Shigeng, Yinggang Li, Xuan Liu, Song Guo, Weiping Wang, Jianxin Wang, Bo Ding, and Di Wu. "Towards real-time cooperative deep inference over the cloud and edge end devices." Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies 4, no. 2 (2020): 1-24.
[4] Banitalebi-Dehkordi, Amin, Naveen Vedula, Jian Pei, Fei Xia, Lanjun Wang, and Yong Zhang. "Auto-split: A general framework of collaborative edge-cloud AI." In Proceedings of the 27th ACM SIGKDD Conference on Knowledge Discovery & Data Mining, pp. 2543-2553. 2021.

## Slide 11: Inference Performance Predictor Existing Works
LPM-TPU[1]
NP-NAS[2]
BRP-NAS (Eagle)[3]
Nn-Meter[4]
PerfSAGE[5]
Notes: [1]: Kaufman, S., Phothilimthana, P., Zhou, Y., Mendis, C., Roy, S., Sabne, A., and Burrows, M. A learned performance model for tensor processing units. Proceedings of Machine Learning and Systems, 3:387–400, 2021.
[2]:
[3]:
[4]:
[5]:

## Slide 12: Inference Performance Predictor Existing Works
MicroNets[1]:
TinyMLPerf[2]: overall performance of TinyML models.
Notes: [1]: Banbury, C., Zhou, C., Fedorov, I., Matas, R., Thakker, U., Gope, D., ... & Whatmough, P. (2021). Micronets: Neural network architectures for deploying tinyml applications on commodity microcontrollers. Proceedings of machine learning and systems, 3, 517-532.
[2]: Banbury, Colby R., Vijay Janapa Reddi, Max Lam, William Fu, Amin Fazel, Jeremy Holleman, Xinyuan Huang et al. "Benchmarking tinyml systems: Challenges and direction." arXiv preprint arXiv:2003.04821 (2020).

## Slide 13: Questions
1. Per layer execution time
2. How to evaluate search methods?
3. Does the BLE MESH setting affect the applicability of model partitioning?