## Slide 1: Micro-network-project
Xiaoguang Guo

## Slide 2: Outline
1. Overview
2. System Design and Pipeline
3. Existing Works
4. Inference Performance Predictor
5. Insights
6. Search

## Slide 3: 1. Overview
The goal is to optimize the partitioning of DNN models across resource-limited MCU nodes in a BLE mesh network without internet connectivity, focusing on minimizing computation and transfer time while considering memory and energy constraints.
This involves:
  1. How to make multiple MCUs cooperate?
    WiFi and BLE-Mesh
  2. How to run inference on multiple MCUs?
    Model Partitioning

## Slide 4: 2.1 System Design
1. Network Construction
  Network topology
  Roles assignment
  Link
Scheduler
Communication API
Scheduler:
  1. Preconfigure the network
  2. Model partitioning and deployment
  3. Monitor the network (feedback loop)

## Slide 5: 2.1 System Design
Distributed Inference/retraining
Collaborative Virtual Network Our new virtual network
BLE 1.1 Mesh Network
We will use computing/super nodes to establish the distributed learning path on the overlay network.

## Slide 6: 2. 2 Pipeline
1. Network Initialization
2. Profiling
  Network conditions:
    Nodes capabilities(CPU, Memory, Architecture)->processing time
    Network bandwidth -> transfer time
  DNN Model (per layer)
    Latency, memory, energy, data size
3. Model Partitioning
  Per layer execution time (Assume that each layer is independent)
  Assignment(layer-device) determination
4. Model Deployment
  Select virtual ‘routing’ for distributed inference
5. Optimization (optional)
  Feedback loop (Network <-> Model performance)
  Model optimization

## Slide 7
BLE Mesh Network
Overlay Network
Model Partitioning
Scheduler
Profiler
Search
Inference performance predictor for MCUs
Latency
Memory
Energy
Network Conditions
Profiler
Bandwidth
Nodes Capabilities
Routing
Provisioning
Flooding
Data Size
Relaying

## Slide 8: 2. 3 Model Partitioning Pipeline
Determination of assignment(layer-device): (search problem)
  Input(network, model)
    Network(nodes,)
    Model(layers,)
  Output(assignment)
Model partition:
  Input(assignment, model)
  Output(model segment 1, model segment 2)
Model deployment:
  Model segment 1 -> MCU 1
  Model segment 2 -> MCU 2
  ……

## Slide 9: 3.1 Model Partitioning Existing Works
Applicable Scenarios: Edge-Cloud
Neurosurgeon(ASPLOS’17)[1]:
  Analyze DNN Architecture-> Predict Layer Performance->Evaluate Partition Points->Execute Partitioned DNN
DADS(INFOCOM’19)[2]: Min-Cut
QDMP(IMWUT’20)[3]: Per layer latency is calculated by subtracting the maximum latency of all precursor layers from the total latency up to the current layer.
Auto-Split(KDD’21 ADS Track)[4]: Graph Optimization(Layer folding, layer fusion)
Notes: [1] Kang, Y., Hauswald, J., Gao, C., Rovinski, A., Mudge, T., Mars, J., & Tang, L. (2017). Neurosurgeon: Collaborative intelligence between the cloud and mobile edge. ACM SIGARCH Computer Architecture News, 45(1), 615-629.
[2] Hu, Chuang, Wei Bao, Dan Wang, and Fengming Liu. "Dynamic adaptive DNN surgery for inference acceleration on the edge." In IEEE INFOCOM 2019-IEEE Conference on Computer Communications, pp. 1423-1431. IEEE, 2019.
[3] Zhang, Shigeng, Yinggang Li, Xuan Liu, Song Guo, Weiping Wang, Jianxin Wang, Bo Ding, and Di Wu. "Towards real-time cooperative deep inference over the cloud and edge end devices." Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies 4, no. 2 (2020): 1-24.
[4] Banitalebi-Dehkordi, Amin, Naveen Vedula, Jian Pei, Fei Xia, Lanjun Wang, and Yong Zhang. "Auto-split: A general framework of collaborative edge-cloud AI." In Proceedings of the 27th ACM SIGKDD Conference on Knowledge Discovery & Data Mining, pp. 2543-2553. 2021.

## Slide 10: 3.2 Inference Performance Predictor Existing Works
LPM-TPU[1]
NP-NAS[2]
BRP-NAS (Eagle)[3]
nn-Meter[4]
PerfSAGE[5]
Notes: [1]: Kaufman, S., Phothilimthana, P., Zhou, Y., Mendis, C., Roy, S., Sabne, A., and Burrows, M. A learned performance model for tensor processing units. Proceedings of Machine Learning and Systems, 3:387–400, 2021.
[2]: Wen, Wei, Hanxiao Liu, Yiran Chen, Hai Li, Gabriel Bender, and Pieter-Jan Kindermans. "Neural predictor for neural architecture search." In European Conference on Computer Vision, pp. 660-676. Cham: Springer International Publishing, 2020.
[3]: Dudziak, Lukasz, Thomas Chau, Mohamed Abdelfattah, Royson Lee, Hyeji Kim, and Nicholas Lane. "Brp-nas: Prediction-based nas using gcns." Advances in Neural Information Processing Systems 33 (2020): 10480-10490.
[4]: Zhang, Li Lyna, Shihao Han, Jianyu Wei, Ningxin Zheng, Ting Cao, Yuqing Yang, and Yunxin Liu. "Nn-meter: Towards accurate latency prediction of deep-learning model inference on diverse edge devices." In Proceedings of the 19th Annual International Conference on Mobile Systems, Applications, and Services, pp. 81-93. 2021.
[5]: Chai, Yuji, Devashree Tripathy, Chuteng Zhou, Dibakar Gope, Igor Fedorov, Ramon Matas, David Brooks, Gu-Yeon Wei, and Paul Whatmough. "Perfsage: Generalized inference performance predictor for arbitrary deep learning models on edge devices." arXiv preprint arXiv:2301.10999 (2023).

## Slide 11: 3.3 Inference Performance Predictor Existing Works
MicroNets[1]:
TinyMLPerf[2]: overall performance of TinyML models.
Regression model
Notes: [1]: Banbury, C., Zhou, C., Fedorov, I., Matas, R., Thakker, U., Gope, D., ... & Whatmough, P. (2021). Micronets: Neural network architectures for deploying tinyml applications on commodity microcontrollers. Proceedings of machine learning and systems, 3, 517-532.
[2]: Banbury, Colby R., Vijay Janapa Reddi, Max Lam, William Fu, Amin Fazel, Jeremy Holleman, Xinyuan Huang et al. "Benchmarking tinyml systems: Challenges and direction." arXiv preprint arXiv:2003.04821 (2020).

## Slide 12: 4. Inference Performance Predictor
Datasets
  Latency datasets:
    The latency for various MCUs, across different types of layers and sizes, is measured using TensorFlow Lite for Microcontrollers (TFLM).
  Memory footprint datasets:
    Simulation on Server?
  Energy consumption datasets:
Predictor(MCU, Layer) =
  Latency
  Memory footprint (memory, storage)
  Energy consumption
Notes: [1]: Banbury, C., Zhou, C., Fedorov, I., Matas, R., Thakker, U., Gope, D., ... & Whatmough, P. (2021). Micronets: Neural network architectures for deploying tinyml applications on commodity microcontrollers. Proceedings of machine learning and systems, 3, 517-532.

## Slide 13: 5. Insights
1. Per layer latency
2. Data size distribution
Notes: [1]: Zhang, Shigeng, Yinggang Li, Xuan Liu, Song Guo, Weiping Wang, Jianxin Wang, Bo Ding, and Di Wu. "Towards real-time cooperative deep inference over the cloud and edge end devices." Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies 4, no. 2 (2020): 1-24.

## Slide 14: 6. Search
Cost Function: multi-objectives search
.
Linear:
Or non-linear:
How to find a cost function?

## Slide 15: 6. Search
Insights:
  Memory Constraints First(hard conditions)
  Latency-Intensive Layers to powerful devices

## Slide 16: 6. Search
Computation and transfer time:
1. Layer-Device Assignment Matrix (X)
  Represents which device each layer is assigned to.
  Rows correspond to layers, and columns correspond to devices.
  A ‘1’ in the matrix indicates the layer is assigned to that device.
2. Transfer Time Matrix (T)
  Represents the time required to transfer data between devices.
  Rows and columns correspond to devices.
  An element T[i,j] indicates the time to transfer data from Device i to device j.
3. Computation Time Matrix (C)
  An element C[i,j] indicates the computation time that device j process layer i

## Slide 17: 6. Search Methods
Greedy Algorithm
Simulated Annealing
Genetic Algorithm
Particle Swarm Optimization
Ant Colony Optimization
Branch and Bound
Hill Climbing
Random Search
Mixed-Integer Linear Programming
Tabu Search
Table: Performance Comparison of Different Partitioning Algorithms for Layer-Device Assignment in Distributed Inference on a 6-Layer Model Across 5 Devices

## Slide 18: Questions
1. Per layer execution time
2. Feedback: model <-> network
2. How to evaluate search methods?
4. Contributions

## Slide 19
Memory should also be a problem. Like how to measure it? How to evaluate it?
Search method
Memory trend
Model layer data size figure

## Slide 20
Different memory components of one single device
How program be stored in MCUs
  Data
  Graph
  Parameters
  Output
How to evaluate the memory footprint
  For the memory trend
We should also consider ble mesh firmware