## Slide 1: Enabling Decentralized Machine Learning on heterogeneous Microcontroller Networks.
Xiaoguang Guo
5/5/2024

## Slide 2
CPS
Resources reallocation
Data
CPU-GPU co-run
Compressed Data
Data transmission
Hardware
Model compression
Data redundancy elimination
Data redundancy
On-device learning
Decentralized
Distributed
Architecture
CPU-GPU Integrated
ARM CPU
MCUs
Workload detection
Federated
Streaming-data
Process directly without decompression
Cross devices
Notes: Distributed framework regular
MCUs how to communication
6iowpm bluetooth jig B limited
Target to which level MCUs
Wifi or

## Slide 3
Background:
  IoT ↑, MCUs
  EdgeAI & AIoT: On-device learning, TinyML(Cloud -> MCUs)
  Distributed learning: local learning -> FL -> swarm learning
  Despite progress in decentralized and swarm learning, significant gaps persist at the microcontroller level.
Research Problem:
  Can we design a data-driven, decentralized MCUs system utilizing swarm learning to solve real-world problems?
Contributions:
  Swarm Learning Framework for Multi-Device Collaboration on MCUs.
  Development of an Efficient Communication Protocol for Decentralized MCU Networks.

## Slide 4
Smart Agriculture
  Soil moisture, auto irrigation, pest activity, nutrient levels,…
Environmental Monitoring
  Air & water quality, forest fires, illegal logging in remote areas
Health Monitoring
  Emergency alert
Industrial IoT
  Maintenance of machinery
Smart Cities
  Traffic flow management
Wildlife tracking and conservation
  Monitoring wildlife movements

## Slide 5
Research questions:
  How can swarm learning algorithms on MCUs be optimized for energy and computational efficiency in a decentralized network?
  What communication protocols best support robust and efficient data exchange in intermittently connected decentralized MCU networks?
  How can the network topology of decentralized MCU systems be dynamically managed to optimize learning and communication as nodes change?
  What are the trade-offs between accuracy and efficiency in decentralized learning systems on MCUs?
  How can machine learning models in decentralized MCU networks be dynamically adjusted in response to environmental changes?

## Slide 6
System Architecture
  MCUs Selection:
  Sensor Integration:
  Communication Infrastructure
    Heterogeneous Communication System
Swarm Learning Algorithms
  Algorithms Selection
  Customization
  Simulation

## Slide 7
Communications Protocols:
Protocol | Description | MCUs Examples | Applications
Wi-Fi | TCP/IP, wide range | ESP8266, ESP32 | Smart home, IoT,
BLE | Short range, low power | nRF52840, ESP32 | Wearables
Zigbee | Mesh networking, | Xbee modules, CC2530 | Home automation
LoRa | Long range, rural areas | STM32(SX1278) | Agricultural sensors
CAN | Robust, noisy env, automative | ATmega32M1, STM32 | Automative networks
NFC | Very short range, secure | PN532 NFC, STM32 | Contactless payments

## Slide 8
Begin with 3 MCUs.
  Homogeneous (identical MCUs) or heterogeneous (different MCUs)?
  One communication protocol or multiple protocols
  Multiple tasks simultaneously or one single task distributed?

## Slide 9
Communication Network Architecture
  Peer-to-peer, Dynamic Mesh Topology
  Nodes: ESP32
  Protocols:
    Wi-Fi Direct (no need Wi-Fi AP)
    BLE?
    Best path for data packets

## Slide 10
MCUs selection: ESP32-WROVER
https://www.amazon.com/gp/product/B0B3JD1K1T/ref=ox_sc_act_title_1?smid=A3S807LE0L63AP&psc=1 https://www.amazon.com/Freenove-ESP32-WROVER-Bluetooth-Compatible-Tutorials/dp/B0CJJHXD1W/ref=sr_1_2?crid=F1E4RMJ0368C&dib=eyJ2IjoiMSJ9.qRWqoY_UasjKo8Ke477M5cCkEpLxcPZqIAzXzRbPz-kVq5RbFAECDwEmGCtijln69j0TlvTjtibegiWc7lkIehlRMlnL7-UJEp_XkSgDB9whYNWhHsj-R9CdxqcuGV1IrYO6HDycrHPRSqW75PRFs_APxhMcHc7xtOMq_2E9I5bF_s-or5yihVbL9QRVQyKbtCmU5cJ4JLpJI5KJWO-52Nkx4k3YA15Gw2Tx2kA13G8.NP8mD56wBrTqJJQHvm9kXCRnOug7k8xrEhyc3TJV-pI&dib_tag=se&keywords=ESP32-WROVER&qid=1715748951&sprefix=esp32-wrover%2Caps%2C153&sr=8-2&th=1

## Slide 11
Machine Learning Tasks:
  Phase 1 (preloaded dataset)
    Simulating real-world data distribution
    Same Pre-built models on 3 devices
    Existing frameworks: TensorFlow Lite, MicroML, …
  Phase 2 (real-world application)
    Sensors integration: Collecting data from each device

## Slide 12
TinyML Frameworks:

## Slide 13
A Systematic Literature Review on Distributed Machine Learning in Edge Computing
  Table 8. EI frameworks
If applicable, decentralized learning frameworks
SWARM LEARNING: A SURVEY OF CONCEPTS, APPLICATIONS, AND TRENDS
Maybe MCUs network

## Slide 14
System Objectives?
Hardware
  AI accelerators?
  Peripheral Integration: Sensors and actuators
  Power
Decentralized Network Architecture
  Topology Design: peer-to-peer?
  Communication Protocol: Zigbee, bluetooth, LoRa
AI and Swarm Learning Components
  AI Model Development: Pruning, Quantization, model compression,…
  Local Learning
  Model Sharing Mechanism
  Blockchain protocol
Software Development
  Firmware Development: data collection, local processing, and communication
  Swarm Intelligence Algorithms: collaboration and adaptation

## Slide 15: Notes before May 14th, 2024
We want to evaluate both BLE and Wi-Fi.
https://www.amazon.com/gp/product/B0B3JD1K1T/ref=ox_sc_act_title_1?smid=A3S807LE0L63AP&psc=1 https://www.amazon.com/Freenove-ESP32-WROVER-Bluetooth-Compatible-Tutorials/dp/B0CJJHXD1W/ref=sr_1_2?crid=F1E4RMJ0368C&dib=eyJ2IjoiMSJ9.qRWqoY_UasjKo8Ke477M5cCkEpLxcPZqIAzXzRbPz-kVq5RbFAECDwEmGCtijln69j0TlvTjtibegiWc7lkIehlRMlnL7-UJEp_XkSgDB9whYNWhHsj-R9CdxqcuGV1IrYO6HDycrHPRSqW75PRFs_APxhMcHc7xtOMq_2E9I5bF_s-or5yihVbL9QRVQyKbtCmU5cJ4JLpJI5KJWO-52Nkx4k3YA15Gw2Tx2kA13G8.NP8mD56wBrTqJJQHvm9kXCRnOug7k8xrEhyc3TJV-pI&dib_tag=se&keywords=ESP32-WROVER&qid=1715748951&sprefix=esp32-wrover%2Caps%2C153&sr=8-2&th=1

## Slide 16
Swarm learning is an overlay network.
  Block chain is necessary for all current system setup.
  For micro controller local network, is block chain feasible?
  What kind of block chain platform or market is assumed or built on?
Distributed or decentralized on micro-controller ML learning.
  Multiple local devices (who distributes IPs)
  No centroid node.
  Wi-Fi or Bluetooth?

## Slide 17: https://www.dusuniot.com/blog/bluetooth-iot-deploying-your-iot-projects-with-ease-and-low-cost/

## Slide 18
Feature | Bluetooth Classic | Bluetooth Low Energy (BLE)
Frequency Range | 2.402GHz to 2.48GHz | 2.402GHz to 2.48GHz
Range | Up to 100 meters | Up to 100 meters
Data Transfer Rate | 1-3 Mbps | 125 Kbps – 2 Mbps
Communication Mode | Continuous | Short bursts
Power Consumption | Higher | Lower
Voice & Large File Transfer | Yes | No
Latency | Up to 100ms | 6ms
Power Usage | 1 Watt | 0.01 to 0.5 Watts
Bidirectional Communication | Yes | Yes
Unidirectional Communication | No | Yes
Indoor Location Tracking | Limited accuracy | Yes
Asset Management | Limited tracking capabilities | Yes
PC Peripherals Support | Yes | Limited support
Security | AES-128 encryption | AES-128 encryption

## Slide 19
Is block chain feasible?
Lightweight Blockchain Protocols:
  Tangle (IOTA): Utilizes a directed acyclic graph reducing resource consumption.
  Nano’s Block-Lattice
Consensus Mechanism:
  Proof of Authority (PoA): Selected nodes (authorities) validate transactions, reducing computational load.
  Delegated Proof of Stake (DPoS): Stakeholders vote for a small number of delegates to validate transactions.
  Practical Byzantine Fault Tolerance (PBFT): Optimized for low-latency networks with known participants
Hybrid Blockchain IoT networks

## Slide 20
Step | Component(s) Involved | Description | Hardware Specifications
Node Initialization | ESP32-WROVER, Blockchain Client | Initialize the ESP32-WROVER nodes and set up blockchain clients. | Dual-core Xtensa LX6, 240 MHz, 8MB PSRAM, 4MB Flash
Data Collection | ESP32-WROVER, Sensors | Collect sensor data (e.g., temperature, humidity, air quality) from the environment. | Various sensors connected via GPIO, I2C, SPI, UART
Data Preprocessing | ESP32-WROVER | Preprocess collected data (e.g., noise reduction, normalization) before training. | Dual-core Xtensa LX6, 240 MHz
Local Model Training | ESP32-WROVER, TinyML Frameworks | Train local ML models using the preprocessed data. | TensorFlow Lite for Microcontrollers, uTensor, 8MB PSRAM
Model Update Creation | ESP32-WROVER, Blockchain Client | Create a blockchain transaction containing the local model update (parameters). | Integrated blockchain client, 4MB Flash
Transaction Signing | ESP32-WROVER, Crypto Engine | Sign the transaction using the node’s private key to ensure authenticity. | AES, SHA-2, RSA, ECC
Transaction Broadcasting | ESP32-WROVER, Communication Module | Broadcast the signed transaction to other nodes in the network. | Wi-Fi 802.11 b/g/n, Bluetooth 4.2
Consensus Mechanism | ESP32-WROVER, Blockchain Network | Validator nodes verify transactions and add them to the blockchain. | Integrated blockchain client, PoA or DPoS consensus
Model Aggregation | ESP32-WROVER, Smart Contracts | Smart contracts aggregate model updates from different nodes into a global model. | Integrated blockchain client, Smart Contracts
Global Model Deployment | ESP32-WROVER, TinyML Frameworks | Deploy the aggregated global model to all nodes for inference. | TensorFlow Lite for Microcontrollers, uTensor
Inference and Action | ESP32-WROVER, Sensors, Actuators | Use the global model for real-time predictions and trigger actions based on predictions. | Dual-core Xtensa LX6, 240 MHz, various sensors and actuators
Data Persistence and Storage | ESP32-WROVER, Flash Memory | Store critical data, model parameters, and blockchain ledger in Flash memory to ensure data persistence. | 4MB Flash Memory

## Slide 21
Component | Specifications | Role
ESP32-WROVER Node | Dual-core Xtensa LX6, 240 MHz 8MB PSRAM 4MB Flash Wi-Fi 802.11 b/g/n, Bluetooth 4.2 | Main node for data collection, preprocessing, local model training, and blockchain operations.
Sensors | Connected via GPIO, I2C, SPI, UART | Collect environmental data (e.g., temperature, humidity, air quality).
Data Collection | Using sensor interfaces | Collect data from sensors for processing.
Data Preprocessing | Dual-core Xtensa LX6 | Clean and normalize collected data for model training.
Local Model Training | TensorFlow Lite for Microcontrollers, uTensor, … | Train ML models using preprocessed data.
Inference | Using trained ML models | Make predictions based on new sensor data.
Storage (Flash) | 4MB Flash Memory | Store critical data, model parameters, and blockchain ledger.

## Slide 22
Component | Specifications | Role
Blockchain Client | Software running on ESP32-WROVER | Manages blockchain transactions, consensus participation, and smart contract execution.
Transaction Creation | Using local data and model updates | Create blockchain transactions with collected data or model parameters.
Transaction Signing | AES, SHA-2, RSA, ECC | Sign transactions using cryptographic keys to ensure authenticity.
Consensus Participation | PoA or DPoS consensus | Participate in the consensus process to validate transactions and add blocks to the blockchain.
Model Aggregation | Using smart contracts | Aggregate model updates from different nodes into a global model.
Smart Contracts | Executed on the blockchain | Automate actions based on blockchain data (e.g., reward distribution).
Global Model Deployment | Deploying aggregated model | Deploy the global model to all nodes for inference.
Data Persistence | Storing in Flash memory | Ensure critical data is securely stored and remains persistent across power cycles.

## Slide 23
Part | Components | Action
Model Update Creation | ESP32-WROVER, TensorFlow Lite for Microcontrollers | - Train the local model on preprocessed data. - Extract model parameters (e.g., weights). - Create a transaction: `{ "node_id": "Node1", "model_update": { "weights": [0.1, 0.5, ...], "biases": [0.3, 0.7, ...] }, "timestamp": "2024-05-15T12:00:00Z" }`
Model Sharing | ESP32-WROVER, Blockchain Client | - Sign the model update transaction using the node’s private key. - Broadcast the signed transaction to other nodes in the network using Wi-Fi or BLE.
Model Aggregation | Smart Contracts, Blockchain Network | - Collect model updates from various nodes. - Execute smart contracts to aggregate model updates: - Aggregation formula: `Global Weight = (1/N) Σ Node Weight_i` - Store aggregated model parameters on the blockchain.
Global Model Deployment | ESP32-WROVER, Blockchain Client | - Monitor the blockchain for new global model updates. - Retrieve the aggregated global model parameters. - Update the local model with the new global parameters: `updateModel(globalParams)`

## Slide 24
R

## Slide 25
Research Goals:
  Minimizes Energy Consumption
  Maximizes Performance
  Handles Randomness and Uncertainty
Challenges:
  Data Distribution
  Decentralized Coordination
  Energy Efficiency
  Dynamic Synchronization
  Subset Selection for Training
  Communication Protocols

## Slide 26
Research Questions
  How to design energy-efficient swarm learning algorithms for MCUs?
  What are the optimal communication protocols and synchronization strategies for decentralized MCU networks?
  How to dynamically manage the network topology and MCU participation to optimize learning efficiency and energy consumption?
  What are the trade-offs between training on subsets of MCUs versus the entire network?

## Slide 27
Theoretical Framework
Energy Consumption Model

## Slide 28
Synchronization and Training Strategy

## Slide 29
Objective Function:
  Minimize the total energy consumption while maximizing model performance.
Constraints:
  Ensure communication delays L are minimized.
  Meet a minimum accuracy threshold A_min
  Adapt to dynamic availability and participation of MCUs.

## Slide 30
Data Distribution
Data bias
Do we need to redistribute data?

## Slide 31
Global model

## Slide 32
R
https://www.youtube.com/watch?v=e7o2C0lPrKg
Model parallel

## Slide 33
Dist

## Slide 34
Distributed communication:
  All-Reduce Ring

## Slide 35
Dist

## Slide 36: BLE

## Slide 37: BLE
Bluetooth Mesh Networking
  Managed flooding

## Slide 38: BLE

## Slide 39: BLE

## Slide 40: BLE